PWM deed moeilijk bij endstops

digital pins, input is default 0 1 2 ...
pinMode INPUT OUTPUT INPUT_PULLUP
digitalRead (works on both input and output)
digitalWrite HIGH LOW

analog A0, A1, A2,...
analogRead
(pinMode is not for analog, configures them as digital, but analogRead overwrites them back to input)
analogWrite (output only, sets to output, works with PWM pins)

Left right movement: X
forward, backward, Y
up down Z
floorchange F
Tool 1
Tool 2
...

Stepper controller: Enable, Pulse, Direction

Enable for floorchangers
Enable for X,Y,Z, tools (together)

Pulse X 52
Pulse Y 48
Pulse Z 44
Pulse F 40
Pulse T1 36

Dir X 53
Dir Y 49
Dir Z 45
Dir F 41
Dir T1 37

Endstop min X 50
Endstop min Y 46
Endstop min Z 42
Endstop min F 38
Endstop min T1 34
Endstop max T1 35(als na x stappen max niet bereikt, dan heeft ie iets vast, veren)

2+5+5+6 = 19